## Slide 1: Conceptual Model Project
Secondary Stakeholders
Workshop 2
Incorporate feedback
Primary Stakeholders
Workshop 1
Incorporate feedback
Core Science Team
Identify key technical barriers
Refine services/products
Seed Concept
Establish Core Principles
Final Conceptual Model
Refine conceptual model
Refine conceptual model
Road map for services/products
Level of Effort
Scope development and support
Define milestones
January
February
March
April
May
June
2021
Guiding Principles
Fire emissions inventories (EIs) used for regulatory and research applications are not typically developed with data quality standards and metadata requirements like EIs developed for other significant source sectors
Need for services/ products that provide vetted, metadata-rich fire EIs for modeling and analysis applications at defined levels of quality
Need for long-term support for fire emissions products or services to maintain consistency and continuity for stakeholders
Conceptual Model For Long-Term Fire Data Support (wrapair2.org)
Notes: Slide on current active project. ‘Conceptual Model For Long-Term Fire Data Support’. Example of FSWG team project. BOB (Matt Mavko to provide a slide or two – where we are at)
the goal of this project is to establish technical standards and identify products and services needed for long-term availability of high-quality fire emissions data
Summary of where this project is at.

## Slide 2: Conceptual Model (CM) Project Status
Accomplishments to date
  Formed a Core Science Team (CST) of EI practitioners and data providers
  5 CST meetings to develop CM requirements and technical steps
  Invited two Subject Matter Experts to provide input and feedback on CM concepts
Upcoming activities
  Finalize CM technical steps with targeted case studies exercising specific concepts
  Finalize Data Warehouse concept and reach out to potential grant partners
  Convene workshops with groups of stakeholders to introduce CM concepts, review technical details, and explore applications
Notes: Slide on current active project. ‘Conceptual Model For Long-Term Fire Data Support’. Example of FSWG team project. BOB (Matt Mavko to provide a slide or two – where we are at)
the goal of this project is to establish technical standards and identify products and services needed for long-term availability of high-quality fire emissions data
Summary of where this project is at.

## Slide 3
BAER/
BARC
FEPS
HMS
Annual Fire Geography
Burn Severity
MTBS
WFAS fuel moisture
Event
Location; start date; growth cessation date; out date; smoldering stopped date
Activity
Acres or tons/day; burn type; fuel type; fuel loading; fuel moisture
FCCS - fuel type & loading; WFAS – fuel moisture; burn type – reporting/permits; spatiotemporal rules
Consumption
Tons burned
BlueSky modeling framework; FOFEM; reporting/permits; assumptions
Emission Factors
Emissions Inventory
Mass pollutant/ton burned
Tons pollutant/day
AP-42; Missoula Lab; other references; embedded in consumption/emission calculation frameworks
Sources of Data: Wildfire – SMARTFIRE, ICS209, FRAP (CA); Rx – burn permit databases. Satellite Detects – all types of fire with sufficient heat signature; effort to categorize and cross-check
2 Years
1 Year
6 months
Real-Time
NIFS (InForms)
SERA
NAWFD
LANDFIRE Vintage
CONSUME
FOFEM
Default Fire Geography
FINN
BlueSky Pipeline
NPS
MODIS MCD64A1
Level 0
Level 1
Level 2
Primary
Data/Tool
Helper or Enhancer
FCCS/EVT Grid
SMARTFIRE v2
FRAP Database
SMP Permits
NASF
VIIRS AFP
Available Components, Data Timing, Quality
Infrared datasets

## Slide 4
BAER/
BARC
Infrared datasets
FEPS
HMS
Annual Fire Geography
Burn Severity
MTBS
WFAS fuel moisture
Event
Location; start date; growth cessation date; out date; smoldering stopped date
Activity
Acres or tons/day; burn type; fuel type; fuel loading; fuel moisture
FCCS - fuel type & loading; WFAS – fuel moisture; burn type – reporting/permits; spatiotemporal rules
Consumption
Tons burned
BlueSky modeling framework; FOFEM; reporting/permits; assumptions
Emission Factors
Emissions Inventory
Mass pollutant/ton burned
Tons pollutant/day
AP-42; Missoula Lab; other references; embedded in consumption/emission calculation frameworks
Sources of Data: Wildfire – SMARTFIRE, ICS209, FRAP (CA); Rx – burn permit databases. Satellite Detects – all types of fire with sufficient heat signature; effort to categorize and cross-check
2 Years
1 Year
6 months
Real-Time
NIFS (InForms)
SERA
NAWFD
LANDFIRE Vintage
FOFEM
Default Fire Geography
FINN
BlueSky Pipeline
NPS
MODIS MCD64A1
Level 0
Level 1
Level 2
Primary
Data/Tool
Helper or Enhancer
FCCS/EVT Grid
SMARTFIRE v2
FRAP Database
SMP Permits
NASF
CONSUME
NIFS + HMS for daily WF activity
Point Reports activity
HMS + fire geography for other activity
Consumption & Emissions for #1 and #2 use Consume, fuels DB, moisture
#3 uses FRP for consumption, SERA for emissions
#1 and #2 can use WFEIS, #3 cannot
VIIRS AFP
CMFD Level 1-2 Fire EI Components

## Slide 5
Complete Activity
Reconciled, Classified short-duration fires
Daily Apportioned Wildfire
Classified consumption events
Daily Apportioned Wildfire
HMS
Fire Geography
NIFS (InForms)
SMP Permits
HMS leftovers
Rulesets:
Associate HMS data
Determine Fire End Dates
Fill Time Gaps
Assign Growth Curves
GOES AFP Profiles
Burn Severity
Consumption Events
Rulesets:
Cluster detections
Assign growth profile
Calculate cluster centroid
Estimate tons from FRP
Rulesets:
Match consumption events with reports
Reconcile based on user selection
Base Fire Activity Development Steps
Notes: Add concept of cycle times
Explanation of metadata for WFEIS
WFEIS components
Quality levels and their meaning based on different applications of data (see Data Warehouse document)

## Slide 6
Complete Activity
Reconciled, Classified short-duration fires
Daily Apportioned Wildfire
IWDW Data Warehouse
WFEIS Emissions Calculator
WFAS fuel moisture
SERA
CONSUME
FCCS/ EVT Grid
NAWFD
Emissions Output
Base Fire EI Development Steps

## Slide 7: Data Warehouse Concepts
Guiding Principles
Flexibility
  Options at each step
  Upload and examine user data
Transparency
  No black boxes
  Links to documentation and metadata
Guidance
  Guide users through process
  Present unfamiliar data/methods
Stability
  Stable across time
  Available to a wide range of users
Data Products and Services
Comprehensive fire activity datasets for preset domains
Model-ready fire emissions datasets
QA/QC reports accompanying metadata
Multiple cycle times of product availability

## Slide 8: Data Warehouse Products
Hierarchy | Input Datasets and Tools | Timing | Purpose
Level 0 | NIFS (InForm), HMS, Default Fire Geography WFEIS Emissions Calculator | Available annually no later than 6 months after the end of the previous calendar year | Base platform for subsequent levels Rapid-response first-order estimate of daily emissions Estimates of similar quality and resolution as other source categories
Level 1 | Level 0, SMP Reports, Annual Fire Geography WFEIS Emissions Calculator | Available annually no later than 12 months after the end of the previous calendar year | EI analysis and reporting Exceptional Events
Level 2 | Level 1, GOES AFP (diurnal activity), MTBS WFEIS Emissions Calculator | Available annually no later than 18 months after the end of the previous calendar year | Photochemical Grid Modeling (PGM) Suitable for climatology analyses
Specialty | Level 2 with additional reporting | Available as needs arise | Regional Haze Modeling, e.g., future fire scenarios