## Slide 1: Volatile Organic Compound Measurements and Ozone Trends in Tucson
Department of Hydrology and Atmospheric Sciences
University of Arizona
Eric Betterton
Eduardo Saez
Kyle Rine
Kisiel Chapman
Ruby O'Brien-Metzger
Richard Pepel
Diana Picon
Acknowledgements
NASA Space Grant Program

## Slide 2: Objectives
Determine what has caused Tucson ozone levels to exceed the EPA's NAAQS
Measure ambient VOC concentrations in Tucson for the first time
Whether Tucson is VOC-limited or NOx-limited
Quantify the contribution of biogenic VOCs to ozone production in Tucson

## Slide 3
Collection and Concentration
Chromotography
Analysis (FID)
Materials and Methods
Cryotrap, Thermal Desorber and Gas Chromatograph Physics/Atmospheric Sciences Rooftop lab ​

## Slide 4: Standard A Column

## Slide 5: Sample Collection March 2019 to Present
Rooftop
N = 12,000
Suma cannisters
N = 60

## Slide 6
Sampling Locations​

## Slide 7
Chart: Site
| Children's Park | Saguaro Desert | Downtown | Santa Rita
Average VOC sum | 99.3775 | 90.3967 | 177.6633 | 94.8012
Average Ozone | 47.75 | 48.3333 | 37 | 53.3077
Average NOx | 2.275 | 2.4 | 4.7167 | 1.8918
(4 samples) (3 samples) (6 samples) (13 samples)
Cannister Samples Across Tucson Area

## Slide 8
Chart: Time Sample was Taken
| Morning (Low) | Afternoon
Average VOC Sum | 201.055 | 165.9675
Average Ozone | 25.5 | 43.6667
Average NOx | 8.3 | 3
Tendencies:
High VOC concentration in the morning, low in the afternoon.
Higher NOx concentration in the morning than the afternoon.
Downtown Averages at Highest and Lowest Ozone Levels

## Slide 9: Typical Noon Sample at University of Arizona
(All samples taken at noon.)

## Slide 10: Anthropogenic vs. Biogenic VOCs
Chart: VOC Contribution
| 43990 | 43991 | 43992 | 43993
Alkanes ≤ 5 | 37.43 | 85.48 | 84.64 | 92.92
Alkanes ≥ 6 | 70.01 | 94.68 | 83.2 | 94.82
Alkenes | 9.85 | 19.83 | 44.95 | 23.93
Alkenes (Biogenic) | 0 | 7.95 | 0 | 8
Aromatics | 98.28 | 126.02 | 111.01 | 130.4
Total VOC | 215.57 | 333.96 | 323.8 | 350.07
NOx | 13 | 20.5 | 20.1 | 12.7
Ozone | 53 | 72 | 67 | 78

## Slide 11: VOC Concentration vs. Ozone Concentration
Chart: Daily Max VOCs vs. Ozone - Children's Park
| 43983 | 43984 | 43985 | 43986 | 43987 | 43988 | 43989 | 43990 | 43991 | 43992 | 43993 | 43994 | 43995 | 43996 | 43997 | 43998 | 43999 | 44000 | 44001 | 44002 | 44003 | 44004 | 44005 | 44006 | 44007 | 44008 | 44009 | 44010 | 44011 | 44012 | 44013 | 44014 | 44015 | 44016 | 44017 | 44018 | 44019 | 44020 | 44021 | 44022 | 44023 | 44024 | 44025 | 44026 | 44027 | 44028 | 44029 | 44030 | 44031 | 44032 | 44033 | 44034 | 44035 | 44036 | 44037 | 44038 | 44039 | 44040 | 44041 | 44042 | 44043
VOCs | 376.06 | 307.15 | 308.74 | 215.44 | 251.29 | 216.41 | 334.3 | 324.4 | 350.37 | 229.01 | 423.93 | 347.21 | 485.48 | 204.58 | 383.7 | 194.14 | 386.07 | 349.37 | 307.06 | 322.7 | 407.52 | 439.98 | 221.5 | 387.25 | 301.53 | 200.48 | 209.7 | 247.5 | 269.82 | 284.9 | 273.67 | 223.55 | 307.41 | 315.98 | 259.2 | 255.05 | 203.64 | 243.21 | 265.79 | 224.46 | 208.91 | 237.32 | 292.84 | 376.04 | 498.01 | 220.52 | 238.93 | 239.56 | 267.57 | 234.35 | 273.5 | 268.91 | 283.1 | 312.76 | 266.03
*
*
* Days ozone level exceeded 70 ppb

## Slide 12: NOx Concentration vs. Ozone Concentration
Chart: Daily NOx vs. Ozone - Children's Park
*
*
* Days ozone level exceeded 70 ppb

## Slide 13: Ozone Isopleth - Tucson
Chart: 
Notes: Source: Tucson NOx: PDEQ , Phoenix Ozone: Cracking the AQ Code (AZDEQ), Phoenix NOx: Ozone production rate and hydrocarbon reactivity in 5 urban areas: A cause of high ozone concentration in Houston (Kleinman 2005)

## Slide 14: Conclusion
First VOC measurements taken in Tucson
Over 12,000 data points collected
Isoprene comprised a relatively small portion of the VOCs measured
High VOC to NOx ratio observed in Tucson
Chart: VOC Contribution (June 11, 2020)
| Aromatics | Alkenes (Biogenic) | Alkenes | Alkanes ≥ 6 | Alkanes ≤ 5
 | 130.4 | 8 | 23.93 | 94.82 | 92.92