## Slide 1: GOES FIRE AND SMOKE TOOL (GOFAST): 2020 Pilot

## Slide 2: Take home points
Simple tool for looking quickly at fire progression and activity, based on the GOES IR sensor Fire Radiative Power product
  Near realtime (fire detections from as recently as 30 minutes)
  Also retrospective view at emissions (all you need is an estimated current fire size) going back days, months to see daily growth/emissions
    Can be pulled directly into model runs for source apportionment with multiple overlapping plumes affecting a site, (e.g., Mueller et al., 2020; http://dx.doi.org/10.3390/atmos11090970 )
Like purple air for emissions
  Good at relative, not necessarily absolute (we’re working on that paper), day to day trends
    E.g., lot of night time activity, post-NIROPs
  Useful for understanding the contribution of fire activity to forecasted and previous days AQI
Adds to situational awareness, especially for
  Large fires (can miss acreages under 100 acres or heat obscured by clouds or thick smoke)
  Remote deployment/pre-deployment
  Area Command sitches where multiple interacting (even joining) fires create too much “perimeter spaghetti” to untangle

## Slide 3
2020-09-04
Fire activity/Fire Growth

## Slide 4: Multiple fires, Large area retrospective on relative daily emissions:
Chart: Provisional Estimate of 2020 CA Daily Fire Emissions (Relative Values Using GOFAST FEER Algorithm, subject to revision*)
| 7/21/2020 | 7/27/2020 | 7/28/2020 | 7/29/2020 | 7/30/2020 | 7/31/2020 | 8/1/2020 | 8/2/2020 | 8/4/2020 | 8/6/2020 | 8/8/2020 | 8/9/2020 | 8/10/2020 | 8/11/2020 | 8/12/2020 | 8/14/2020 | 8/15/2020 | 8/16/2020 | 8/17/2020 | 8/18/2020 | 8/19/2020 | 8/20/2020 | 8/21/2020 | 8/22/2020 | 8/23/2020 | 8/24/2020 | 8/25/2020 | 8/26/2020 | 8/27/2020 | 8/28/2020 | 8/29/2020 | 8/30/2020 | 8/31/2020 | 9/1/2020 | 9/2/2020 | 9/3/2020 | 9/4/2020 | 9/5/2020 | 9/6/2020 | 9/7/2020 | 9/8/2020 | 9/9/2020 | 9/10/2020 | 9/11/2020 | 9/12/2020 | 9/13/2020 | 9/14/2020 | 9/15/2020 | 9/16/2020 | 9/17/2020 | 9/18/2020 | 9/19/2020 | 9/20/2020 | 9/21/2020 | 9/22/2020 | 9/23/2020 | 9/24/2020 | 9/25/2020 | 9/26/2020 | 9/27/2020 | 9/28/2020 | 9/29/2020 | 9/30/2020 | 10/1/2020 | 10/2/2020 | 10/3/2020 | 10/4/2020 | 10/5/2020 | 10/6/2020 | 10/7/2020 | 10/8/2020 | 10/9/2020 | 10/10/2020 | 10/11/2020 | 10/12/2020 | 10/13/2020 | 10/14/2020 | 10/15/2020 | 10/16/2020
Creek | 2.595 | 18298.7311 | 30390.5215 | 12551.565 | 15646.9629 | 2646.071 | 1491.5926 | 645.9558 | 1568.9727 | 8161.4828 | 1165.6383 | 1445.125 | 8762.9805 | 2790.8562 | 11.3185 | 45.9806 | 718.0848 | 2608.9067 | 463.7866 | 145.6169 | 75.0706 | 81.1617 | 21.9282 | 574.5368 | 725.8286 | 169.184 | 40.7137 | 134.7977 | 278.8627 | 336.0567 | 2088.8657 | 261.8122 | 220.5173 | 231.113 | 52.6115 | 0.25779 | 2.5687 | 60.5335 | 289.6287 | 95.831 | 3981.2807 | 731.1885 | 15.2494
SQF Complex | 245.0545 | 451.8114 | 746.8412 | 1810.1844 | 835.6669 | 0.29347 | 291.0978 | 895.0927 | 796.29 | 306.365 | 124.2473 | 240.0059 | 834.7641 | 2755.3025 | 1578.2747 | 1131.4925 | 1343.0845 | 146.3501 | 83.295 | 105.2878 | 9.0591 | 212.416 | 4130.1588 | 7935.3444 | 4681.5267 | 1151.9372 | 2077.7879 | 813.0427 | 213.497 | 146.6761 | 1003.193 | 381.912 | 301.5721 | 139.0318 | 10.1503 | 0.48794 | 20.0639 | 83.2088 | 13.1234 | 3.7816 | 2.8208 | 507.4131 | 13.3523 | 67.281 | 9.0954 | 44.3216 | 353.6481 | 134.3877 | 0.91907 | 6.0094 | 9.3309 | 0.67062 | 8.76 | 5.4769
Slater | 34107.5733 | 20390.17 | 556.8748 | 48.318 | 78.7244 | 49.1579 | 241.1991 | 252.7505 | 17.7147 | 0.36499 | 20.7791 | 8.391
North Complex | 13.6149 | 107.2773 | 2482.9963 | 2512.7534 | 1539.1609 | 457.9011 | 399.7305 | 465.1106 | 83.8487 | 47.7505 | 36.9658 | 113.2177 | 37.6295 | 12.7557 | 389.1465 | 296.336 | 119.4372 | 73.8585 | 727.0656 | 24.1247 | 10.683 | 44118.4266 | 42893.0327 | 604.0849 | 138.4836 | 19.4843 | 577.4205 | 1438.4636 | 784.3663 | 2468.8688 | 936.8352 | 21.4022 | 3.524 | 197.9749 | 67.4396 | 266.8565 | 262.4665 | 21.7121 | 2467.3911 | 3423.9291 | 895.9694 | 99.9956 | 61.0369 | 58.6924 | 22.3798
BluejayWolf (YOSE) | 2.7654 | 141.6263 | 1171.8235 | 24.777 | 0.30478 | 24.3163 | 45.8089 | 0.36275 | 9.8723 | 16.9051 | 6.5422 | 23.5974 | 239.7703 | 137.5697 | 42.0284 | 0.60824 | 1.6139 | 0.0055116
CZU Complex | 0.26298 | 131.1812 | 297.3219 | 5.0962 | 0.64534 | 0.19627
Fork | 435.9622 | 9.9435
Fox | 100.8433 | 15.8881 | 4.5096
Glass | 3877.6561 | 10950.8694 | 528.4677 | 982.2226 | 204.4204
Loyalton | 238.7264 | 4051.1761 | 1600.7537 | 1548.3013 | 9.5048 | 57.0373

## Slide 5: Day to day variation, as it compares to AQI

## Slide 6: Creek Wildfire 9/4-15/2020 – Estimated Daily Acres & PM2.5 Emissions (short tons) Estimates Based on GOES-16 Satellite Data
Progression Map
https://ftp.nifc.gov/public/incident_specific_data/calif_s/!2020_Incidents/CA-SNF-001391_Creek/GIS/Products/20200916/prog_arch_e_land_20200916_2205_Creek_CASNF001391_0909.pdf

## Slide 7
2020-09-04
Fire activity/Fire Growth

## Slide 8
2020-09-05
Fire activity/Fire Growth

## Slide 9
2020-09-06
Fire activity/Fire Growth

## Slide 10
2020-09-07
Fire activity/Fire Growth

## Slide 11
2020-09-08
Fire activity/Fire Growth

## Slide 12
2020-09-09
Fire activity/Fire Growth

## Slide 13
2020-09-10
Fire activity/Fire Growth

## Slide 14
2020-09-11
Fire activity/Fire Growth

## Slide 15
2020-09-12
Fire activity/Fire Growth

## Slide 16
2020-09-13
Fire activity/Fire Growth

## Slide 17
2020-09-14
Fire activity/Fire Growth

## Slide 18
2020-09-15
Fire activity/Fire Growth