## Slide 2
Review upcoming Teach-Ins and participation in WRAP Regional Haze Planning Work Group - Jay Baker and Tina Suarez-Murias

## Slide 3: UNIFORM RATE OF PROGRESS ...AND THE GLIDE PATH – applying this conceptual planning approach
WRAP Regional Haze Planning Work Group
Regional Haze Teach-In #2
July 27, 2017
From Here?
9-15-1982
To There?
10-3-1982

## Slide 4: Conceptual Planning Approach
Focus of 1999 Regional Haze Rule: Achieve Natural Conditions by 2064
  Construct a straight-line Glide Path using deciview units over time
    Start point: Baseline Worst Visibility Averages for 2000-2004
    End Point: Worst Visibility under Natural Conditions, assigned to 2064
    Slope: the Uniform Rate of Progress
  Prepare State SIP with Reasonable Progress Goals (RPGs) for each planning period
    Do interim RPGs land on the Glide Path?
    Why not?
Clean Air Act Amendments of 1977 set National Goal:
    “…the prevention of any future, and the remedying of any existing impairment of visibility in mandatory class I Federal areas which impairment results from manmade air pollution.”
DECIVIEWS
Baseline
(2000-2004)
2018
Best Days Baseline (must not be degraded)
Worst Haze Days Baseline
Uniform Rate of Progress
(Slope of the Glide Path)
2064
Worst Haze Days Average for Natural Conditions
YEAR
Additional time to reach Natural Conditions at initial rate
RPG

## Slide 5: Moving from Concept to Reality
CONCEPT: Assumptions for Achieving Natural Conditions at 2064
Chemical species mass captured on IMPROVE filters, converted to deciviews, quantifies visibility
Natural Conditions are constant and expressed as deciview average for the worst haze days
All anthropogenic impacts can be eliminated, or reduced to be “not perceptible” at monitors
NCII deciview estimates assigned to 2064 can be refined by states with EPA approval
REALITY: Both Natural Conditions and Causes of Haze are changing
Natural sources in West overwhelm anthropogenic reductions on haziest days
Using 2018 RPGs calculated through modeling, Western States set RPGs above the Glide Path
Public considers Glide Path the benchmark of progress and challenged RPGs and initial URPs
Progress is not straight line; 5-year deciview averages do not reflect anthropogenic emission trends
Western visibility improvements not discernible using deciview values alone
Current western visual range on average day is ~111 miles vs. ~58 miles at eastern IMPROVE monitors
Haze Algorithm was refined and estimates of Natural Conditions will change
Climate change, global economy, and political decisions affect natural sources
Deciview
Natural Haze
Anthropogenic Haze
Deciview
Reality: Focus on reducing Controllable Anthropogenic
Uncontrollable Veneer
(Representation of Alaskan site; each site has different mix of these three components)
Initial Concept: Eliminate Anthropogenic Impairment
5

## Slide 6
Redefining Start and End Points of Glide Path
Baseline Years remain Start Point of Glide Path
Same baseline monitoring measurements, reinterpreted for second planning period
Species contributions initially related to emission sources by modeling were quantified
Natural Contributions determined mathematically using percentiles and substitution
Idealized Glide Path still Ends at 2064, but additional adjustments allowed
What will “Natural Conditions” actually be in the future?
Is the NCII or NCIII deciview level for the Worst Haze Days from Natural Sources only?
What deciview quantity actually comes from “uncontrollable sources”?
Should “known” baseline attributions be added to end point as surrogate placeholders?
Beyond 2064, will some of the uncontrollable U.S. anthropogenic emissions become controllable with future “as-yet-unknown” technologies?
U.S. portion of this remaining uncontrollable veneer may or may not become controllable with future unknown technology?

## Slide 7: Glide Path Slope vs Uniform Rate of Progress
Glide Path remains a straight-line benchmark for judging progress
Baseline (start point) and 2064 (endpoint) can change, so long-term slope changes
Baseline will be lower after adjustment to MID
2064 endpoint will be higher after adjustment for “special accounting” emissions
Will 2064 endpoint change with better information incorporated each planning period?
RPG and Uniform Rate of Progress determined for each planning period
Is progress in reducing impairment measured against the RPG or the Glide Path?
Will need some outreach to explain changes to public expectations of progress...
Baseline
(2000-2004)
2064
2018
2028
2038
2048
2058
Initial Glide Path
Adjusted endpoint
(adds components for International Emissions and Prescribed Burning to “Most Impaired Days” for Natural Conditions
2018 RPG
Adjust Baseline starting with Days “Most Impaired” by Anthropogenic Emissions by removing impacts from extreme natural episodic events
DECIVIEWS
YEAR
Best or Clearest Days
Most Anthropogenically Impacted Days (MID)
Worst Natural Haze Days (WND)

## Slide 8
SOURCE | In-State | Out-of-State | International
Anthropogenic | Controllable | not controllable | not controllable
Natural | not controllable | not controllable | not controllable
Focus on Anthropogenic Emissions
1. Define what is Anthropogenic and Controllable
2. Quantify all the emissions contributions on a daily basis for modelling
Figure out relationship between source type and species light extinctions on a daily basis for modelling

## Slide 9: Species’ Light Extinctions vs Source Contributions
Light Extinction Strength does not match relative mass emissions inventory
  Per unit of mass: light extinction EC > OC > Nitrate > Sulfate > Fine Soil > Sea Salt > Coarse Mass
Species Extinction driving Highest Deciview Days in Western baselines different at each monitor
  Mostly OC, Nitrates, Sulfates, and Coarse Mass
  Some natural & some anthropogenic; international sources generate both
Baseline Composition is different on Most Anthropogenically Impaired Days (MIDs)
  Expect Nitrates and Sulfates to dominate; perhaps some OC also
Future Natural Conditions (Worst Natural Haze Days) also estimated by Species Light Extinction
  Expect Natural OC, Coarse Mass, and Fine Soil to be predominant in West
  Is “NCII” (2064 endpoint) realistic? (circa 10 ug/m3 PM10 in top quintile of Worst Natural Haze Days!)
  Is endpoint sum of highest quintile for natural sources of haze?
  How should we quantify international and prescribed fire adjustments to “correct” Natural Conditions?
  What about remaining uncontrollable U.S. anthropogenic emissions?
Farthest Baseline Average Visibility 149 miles for All Days
9.4 >>> 8.0 ug mass
Shortest Baseline Average Visibility 93 miles for All Days
31.3 >>> 7.8 ug mass

## Slide 10: Challenges in Resetting Baseline
Species by species analysis time-consuming, but needed to select percentile
  Compare every year of available data, bay annual average and by every day (for seasonality information)
  Is 95th percentile correct for the specific site for specific species?
  Or any site for any particular year?
Need protocol for daily substitution in days identified with e3 (above selected percentile)
  Seasonal mean? Long-term average? 1x, 2x, 3x median for particular year?
Should every state use both OC+EC along with CM+FS
  Will residential woodsmoke show up?
  Will prescribed fire show up in wildfire percentile?
  Will construction event show up in CM+FS record?
  Will Hawaii be able to pinpoint volcanic emissions using percentile alone?
What to do with sites having <3 years of complete data?
  Data substitution? Include 2005 or later?
Relatively remote site, high elevation, longest data record in California shows change
Understand site context and history, in addition to math!

## Slide 11: Lassen Volcanic Case Study: 95th Percentile
2000 - no wildfires?
2001 - prescribed fires?
2002 - not all of Biscuit Fire?
2003 - maybe no wildfires
2004 - single day spike May 2004
If examined season by season, more likely that 15-30 Mm-1 could be prescribed fires, but over 30 Mm-1 is very likely associated with wildfire smoke – need consultation with Federal Land Managers for confirmation!
Chart: LAVO: OC + EC LIGHT EXTINCTION (2000-2014)
Compare seasonality with known fires and timing of prescribed burns.

## Slide 12: Possible Changes in Outcomes
Each monitor will have new MID baseline dv and long-term Glide Path to adjusted 2064 dv
Within each planning period, the interim URP slope will change
In theory, URP Slope based on 2014 MID dv start and 2028 MID dv forecast
Or, should we model for Worst Haze Days, adjust 2064, and use MID to measure progress?
Chart: YEAR
Rayleigh | 10 | 10 | 10 | 10 | 10 | 10 | 10
OMC | 2.0015 | 17.2 | 37.37 | 1.4937 | 13.5 | 4.5 | 4.5
SO4 | 4.3422 | 6.8 | 5.99 | 2.1184 | 5.2 | 1.2 | 1.2
NO3 | 3.5983 | 3.7 | 2.56 | 2.1339 | 3.2 | 1.6 | 1.6
EC | 3.106 | 3.1 | 5.41 | 3.024 | 2.4 | 0.4 | 0.4
CM | 2.0396 | 2 | 4.05 | 3.486 | 2.1 | 2.4 | 2.4
FS | 0.974 | 1 | 0.96 | 0.778 | 1 | 0.9 | 0.9
Ss | 0.0384 | 0 | 0.13 | 0.184 | 0 | 0.1 | 0.1
2018 RPG (deciviews) | 14.1 | 13.3
Initial URP Path | 14.1 | 14.1 | 7.3
Idealized NCII Glide Path (deciviews) | 14.1 | 14.1 | 7.3
NCII Light Extinction
Initial
Baseline
Worst Haze Days
Light Extinction 2012
Modeled 2018 RPG Extinction
Potential corrections for MID

## Slide 13: Modeling Challenge: Matching Reality
All species unacceptably under-predicted for 2011 base year modeling at SEQU.
How were baseline and NCIII calculated as start and finish of New Glide Path?
Base year projections from 2011 – is West using 2014 as base year for 2028 forecast?
Does 2028 forecast assume natural emissions are the same as 2011 (17-yr. span?)

## Slide 14: Progress Report for 2018
Use Initial Glide Path and 2018 RPG calculation
  Worst Haze Days Average for 2014-2018 (5-yr. avg.)
  Compare with modeled 2018 RFP from initial RH SIP
  Maintain consistency with WHD metric because modeling for 2018 RPGs attempted to account for uncontrollable factors
    Top quintile includes natural & anthropogenic haze
  Review benefits of BART controls after implementation
    Verify emissions reductions of relevant precursors
    Explain light extinction changes observed on Worst Days for species
    Explain whether deciview reduction is discernible
  Potential reasons for differences from modeled 2018 RPGs
    Unexpected growth/decline of species in emissions forecast
    Natural sources emissions different than predicted (e.g. baseline average held constant for wildfires)
    Boundary Conditions changed due to global economy shifts or climate change
  Confirm Best or Clearest Days from Baseline are maintained
  Optional: Compare Visual Range on all days and publicize benefits
Remember: the human eye detects haze at particle concentrations well below the NAAQS health standards!